August 12th 2002

Effect of re-collaring on HCMB__A001-02000013

and comparison with previous experiences

E. Todesco, LHC-MMS-MA

1. Results on HCMB__A001-02000013

- Magnet MCMB__A001-02000013 has been first collared with 0.1 mm and 0.7 mm shim in the inner and outer layer respectively. Magnetic measurements have been performed.

- The collared coil has been de-collared and re-collared with 0.1 mm and 0.8 mm shim. Magnetic measurements have been performed.

- According to simulations, the change in multipoles with respect to the previous collaring should mainly affect C1 (main field) and b3 (sextupole) (see Table I, first line).

- Magnetic measurements show a different effect (see Table I, second to fourth line).

Table I: Effect of a shim change of 0.1 mm on the outer layer: model, measurements on

HCMB__A001-02000013, and discrepancy with respect to model

|  | C1 | b3 | b5 | b7 |
| --- | --- | --- | --- | --- |
| Model | 4.0 | 1.6 | -0.08 | -0.02 |
| 02000013 Aperture 1 | 7.4 | 1.0 | 0.46 | -0.11 |
| 02000013 Aperture 2 | 8.7 | 1.2 | 0.42 | -0.13 |
| 02000013 Average | 8.0 | 1.1 | 0.44 | -0.12 |
| 02000013 Av.-model | 4.0 | -0.5 | 0.52 | -0.10 |

One can make the following remarks:

- The effect is uniform along the axis. The multipole pattern along the axis is similar in the first and in the second collaring (se Fig. 1).

- The effect is very similar in both apertures.

- The peak prestress during collaring went down from 650 bar (first collaring) to 630 bar (second collaring), whist the model foresees a 8.5% increase (i.e., from 650 bar to 705 bar).

Fig. 1: b3 and b5 along the magnet axis measured in the collared coil of HCMB__A001-02000013, first and second collaring

2. Results on HCMB__A001-02000002

- Magnet HCMB__A001-02000002 has been first collared with nominal shims, but with a double coil protection sheet along 1-2 meters in aperture 1.

- The magnet has been decollared, the coil protection sheet removed, and re-collared (no change of shims).

- The expected multipole change in the sections not affected by the double protection sheet is zero. The measured one is shown in Table 2.

Table II: Effect of a re-collaring on magnet HCMB__A001-02000002;

data relative to sections with double protection sheet are not considered.

|  | C1 | b3 | b5 | b7 |
| --- | --- | --- | --- | --- |
| Model | 0.0 | 0.0 | 0.00 | 0.00 |
| 02000002 Aperture 1 | -2.4 | 0.4 | 0.18 | -0.04 |
| 02000002 Aperture 2 | -3.0 | 0.5 | 0.14 | -0.05 |
| 02000002 Average | -2.7 | 0.5 | 0.16 | -0.05 |

- The multipole change is smaller than in the previous case. The variation is similar in both apertures.

3. Comparison between HCMB__A001-02000002, HCMB__A001-02000013 and beam dynamics ranges

- For b5 and b7 the change in HCMB__A001-02000013 is three times of what observed in HCMB__A001-02000002 (see Table III, first and second lines).

- The multipole changes observed in HCMB__A001-02000002 are small compared to the beam dynamics ranges (see Table III, first and third line).

- The b5 change observed in HCMB__A001-02000013 (0.52 units) is a very large fraction of the width of the allowed range for the systematic (0.72 units) and therefore is not negligible. Also for b7 the effect is not negligible.

Table III: Summary of the effect of a de-collaring on multipoles

and comparison with beam dynamics ranges.

|  | C1 | b3 | b5 | b7 |
| --- | --- | --- | --- | --- |
| 02000002 Average | -2.7 | 0.5 | 0.16 | -0.05 |
| 02000013 Av.-model | 4.0 | -0.5 | 0.52 | -0.10 |
| Beam dynamic range | 30.0 | 7.2 | 0.72 | 0.48 |