###### Questions and answers

- Could you tell us more about the planning of the cold mass production?

The sequence adopted should be adequate to satisfy the schedule. We are still at the beginning of the learning curve, having assembled only 10 cold masses. We have progressively modified the assembly sequence and we are now more systematic about the procedure to follow. At the beginning, the production will be surely slower, but we are convinced that 2 cold mass/week will soon become the normal rate in steady conditions. This rate has been computed taking into account 2 shift/day (total time shorter than 16 hours per day, due to the overlap time).

- Do not you think that we need more than 2 welding presses for satisfying the workload?

No, two welding presses should be sufficient for producing 3 cold mass/week. At Rich, the bottleneck was the positioning and welding of the end covers.