Questions and Answers

- What is the cost for the polarity changers for the main power converters?

We hope less than 200.000 SF.

- What is the discharge voltage during the extraction?

The extraction resistance is 40 m( at maximum; the discharge voltage depends on the current. Anyway, this is limited by the protection diodes.

- How many connections do you need for testing the auxiliary bus bars?

About 20.

- How many magnets do you want to equip for doing these tests and what is the additional work for the MMS group?

About sixteen magnets i.e. all the 2001 production for the purpose of the « type test » and then 10% of the total production for the spot checking purpose. The additional work for the MMS group is of only a few days in the first case.