Summary

We present experimental data relative to the azimuthal prestress at 1.9 K and at 300 K in the dipole coils. Data are well fit by a linear relation plus an offset

(w = 0.5 ((c  - 15)   MPa

where (w and (c  are the prestresses at 300 K and 1.9 K respectively. This prestress loss is very relevant (more than 50 %).

Recent improvements of both analytical and finite element codes well reproduce these experimental data, on the basis of the material properties. We observe a small random fluctuation around the fit of around 10 MPa at 99.7 % confidence level. We can claim that prestress loss is under control in the prototypes built so far. The prestress is relevant not only for the maximum field, but also for the field quality, since it gives rise to coil and collar deformations.

We presented the data relative to the warm magnetic measurements. Discrepancies of the odd normal multipoles with respect to the nominal design are mainly determined by the collared coils. We showed that the average offset is due to collar deformations and to the non-negligible magnetic permeability of the collars. The first contribution is expected to be strongly reduced at 1.9 K because of prestress loss. The offset is around -3 units of sextupole and -1.5 units of decapole. The dispersion of the odd multipoles is rather high due to the use of shim thicknesses different from the nominal ones by up to 0.2 mm. This mainly affects the random variation of the sextupole (around 4 units of r.m.s). If this effect is taken out, the dispersion in odd multipoles is in agreement with target values.

Even normal multipoles are due to the magnetic effect of the yoke and of the insert. Assembled cold mass data averaged on the built prototypes show a relevant quadrupole (around 4 units), and rather small octupole (0.3 units). An insert modification has been proposed and successfully tested to reduce both multipoles. The dispersion of the even multipoles is in agreement with target values.

Ezio Todesco

##### Questions and answers

-Which measurements data are available? Where are they?

Permeability at cold temperature, shims and prestress data are available in the group. Permeability at warm temperature was estimated for some samples. All these data are part of the traveler and will be inserted in a database.

-The b2 optimization deteriorates b3 of 0.5 units. Have you taken into account this effect?

b3 can change of 1.5 units from aperture to aperture. It is not meaningful to correct 0.5 units.

-What about the skew component?

No analysis was done yet on skew components.

-Why the three manufacturers use different shims?

Shims were optimized taking into account the prestress at warm. Differences in the azimuthal coil length, according to measurements carried out in the manufacturers, have lead to different shim sizes.