Description of the problem: The measurements of the CCs 1276 (measured on 17-Oct-05) and 1297 (measured on 18-Oct-05) show identical values in the measurement positions 18 and 19, ap.2 and ap.1, respectively. These are the last two positions before the non-connection side coil end. The longitudinal positioning values read out that the mole has not traveled between the two positions, but was stuck.

Request: Could you please check a.s.a.p. the mechanics of the mole as, e.g. the drum, being most likely the source of the problem? For cross-check: the data is available in ITP_21.

# Text boxes

Request for Maintenance/Repair

Date: 19-Oct-05

For: DIMM System 1; used for warm magnetic measurements on collared coils

At: Alstom, Belfort

To: AT-MTM-FM, Juan Garcia Perez, David Giloteaux, Peter Galbraith

From: Christine Vollinger, AT-MAS

CC: G. de Rijk, J-P. Koutchouk